Data Communications
AND Networking
Chapter 3

-------------------------------------------------
ping -c 3 1.1.1.1
PING 1.1.1.1 (1.1.1.1) 56(84) bytes of data.
64 bytes from 1.1.1.1: icmp_seq=1 ttl=58 time=12.4 ms
64 bytes from 1.1.1.1: icmp_seq=2 ttl=58 time=10.6 ms
64 bytes from 1.1.1.1: icmp_seq=3 ttl=58 time=9.87 ms
--- 1.1.1.1 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2002ms
rtt min/avg/max/mdev = 9.868/10.955/12.354/1.038 ms
## Q3-1. What is the relationship between period and frequency?
The relationship is, T = 1 over f , where, T = time period and f = frequency.
## Q3-2. What does the amplitude of a signal measure? What does the frequency of a signal measure? What does the phase of a signal measure?
Amplitude: The amplitude of a periodic variable is a measure of its change in a single period.
Frequency: Frequency is the rate of change with respect to time.
Phase: Phase describes the position of the waveform relative to time 0.
## Q3-3. How can a composite signal be decomposed into its individual frequencies?
A composite signal can be decomposed into its individual frequencies using Fourier transform.
## Q3-4. Name three types of transmission impairment.
Three types of transmission impairment are
1. Attenuation
2. Distortion
3. Noise.
## Q3-5. Distinguish between baseband transmission and broadband transmission.
Baseband: Baseband transmission means sending a digital signal over a channel without changing the digital signal to an analog signal.
Broadband: Broadband transmission or modulation means changing the digital signal to an analog signal for transmission
## Q3-6. Distinguish between a low-pass channel and a band-pass channel.
Low-pass channel: A channel that passes frequencies between 0 and f.
Band-pass channel: A channel that can pass a range of frequencies.
## Q3-7. What does the Nyquist theorem have to do with communications?
The Nyquist bit rate formula defines the theoretical maximum
bit rate and thus helps us to implement a proper method considering the probability of losses.
Q3-8. What does the Shannon capacity have to do with communications?
The Shannon capacity gives us a theoretical highest data rate for a noisy channel.
## Q3-9. Why do optical signals used in fiber optic cables have a very short wave length?
We know that, wavelength = { propagation speed } over frequency . In cables propagation is less than that of vacuums. So the wavelength is kept short.
## Q3-10. Can we say whether a signal is periodic or nonperiodic by just looking at its frequency domain plot? How?
A periodic signal has discrete frequencies, where nonperiodic signal has continuous values.
## Q3-11. Is the frequency domain plot of a voice signal discrete or continuous?
The frequency domain plot of a voice signal will be continuous.
## Q3-12. Is the frequency domain plot of an alarm system discrete or continuous?
The frequency domain plot of an alarm signal will be discrete.
## Q3-13. We send a voice signal from a microphone to a recorder. Is this baseband or broadband transmission?
Sending a voice signal from a microphone to a recorder is generally a baseband transmission.
## Q3-14. We send a digital signal from one station on a LAN to another station. Is this baseband or broadband transmission?
As those two LAN can transfer digital signal, so we don’t need to convert from digital to analogue. Thus it is a broadband transmission.
## Q3-15. We modulate several voice signals and send them through the air. Is this baseband or broadband transmission?
If we modulate multiple signals we have to convert it into a composite signal. Thus broadband is more suitable for it.
## ------- PART TWO -------
## P3-1. Given the frequencies listed below, calculate the corresponding periods.
a.24 Hz
Period = 1 over frequency = 1 over 24 = 0.04167 s
b.8 MHz
Period = 1 over frequency = 1 over { 8 times 10^6 } = 1.27 times 10^-7 s
c.140KHz
Period = 1 over frequency = 1 over { 140 times 10^3 } = 7.143 times 10^-6 s
## P3-2. Given the following periods, calculate the corresponding frequencies.
a.5s
frequency = 1 over {time period} = 1 over 5 = 0.2 Hz
b.12 μs
frequency = 1 over {time period} = 1 over { 12 times 10^-6 } = 8.33 times 10^4 Hz
c.220ns
frequency = 1 over {time period} = 1 over { 220 times 10^-7 } = 45.45 times 10^3 Hz
## P3-3. What is the phase shift for the following?
a. sine wave with the maximum amplitude at time zero
→ 90 degree
b. A sine wave with maximum amplitude after 1/4 cycle
→ 0 degree
c. A sine wave with zero amplitude after 3/4 cycle and increasing
→ 90 degree
## P3-4. What is the bandwidth of a signal that can be decomposed into five sine waves with frequencies at 0, 20, 50, 100, and 200 Hz? All peak amplitudes are the same. Draw the bandwidth.
Bandwidth: 200 Hz (highest frequency) - 0 Hz (lowest frequency) = 200 Hz
## P3-5. A periodic composite signal with a bandwidth of 2000 Hz is composed of two sine waves. The first one has a frequency of 100 Hz with a maximum amplitude of 20 V; the second one has a maximum amplitude of 5 V. Draw the bandwidth.
As the first frequency is 100 Hz and the bandwidth is 2000 Hz, then the second frequency will be 2100.
## P3-6. Which signal has a wider bandwidth, a sine wave with a frequency of 100 Hz or a sine wave with a frequency of 200 Hz?
Bandwidth depends on the frequencies, so 200 Hz has more bandwidth.
P3-7. What is the bit rate for each of the following signals?
a. A signal in which 1 bit lasts 0.001 s
bit rate = 1 over {bit duration} = 1 over 0.001 = 1000 bps
b. A signal in which 1 bit lasts 2 ms
bit rate = 1 over {bit duration} = 1 over {2 times 10^-3} = 500 bps
c. A signal in which 10 bits last 20 μs
bit rate = 1 over {bit duration} = 1 over { 20 times 10^-6 } = 5000 bps
## P3-8. A device is sending out data at the rate of 1000 bps.
a. How long does it take to send out 10 bits?
time period = {number of bit} over {bit rate} = 10 over 1000 = 0.01 s
b. How long does it take to send out a single character (8 bits)?
time period = {number of bit} over {bit rate} = 8 over 1000 = 0.008 s
c. How long does it take to send a file of 100,000 characters?
Let’s assume each character will take approximately 8 bits then we will need (100,000 x 8) or, 800,000 bits.
time period = {number of bit} over {bit rate} = 800,000 over 1000 = 800 s
## P3-9. What is the bit rate for the signal in Figure 3.35?
bit rate = {number of bits} over {bit duration} = 8 over { 16 times 10^-9 } = 5 times 10^8 bps
## P3-10. What is the frequency of the signal in Figure 3.36?
fre quency = {number of full cycles} over {time} = 8 over { 4 times 10^-3 } = 2000 Hz
## P3-11. What is the bandwidth of the composite signal shown in Figure 3.37?

Bandwidth = 5 x 5 = 25 Hz.
P3-12. A periodic composite signal contains frequencies from 10 to 30 KHz, each with an amplitude of 10 V. Draw the frequency spectrum.
## P3-13. A nonperiodic composite signal contains frequencies from 10 to 30 KHz. The peak amplitude is 10 V for the lowest and the highest signals and is 30 V for the 20-KHz signal. Assuming that the amplitudes change gradually from the minimum to the maximum, draw the frequency spectrum.
P3-14. A TV channel has a bandwidth of 6 MHz. If we send a digital signal using one channel, what are the data rates if we use one harmonic, three harmonics, and five harmonics?
As we have 6 MHz, a TV can utilize the whole channel for baseband transmission.
Here more harmonic has more frequencies. First harmonic has only one full cycle for two bits.
So for one harmonic N = f times 2 = 6 times 2 = 12 Mbps
For three harmonic N = f times 2 = 6 times 2 over 3 = 4 Mbps
For five harmonic N = f times 2 = 6 times 2 over 5 = 2.4 Mbps
## P3-15. A signal travels from point A to point B. At point A, the signal power is 100 W. At point B, the power is 90 W. What is the attenuation in decibels?
Attenuation = 10 {log} rsub {10} {{90} over {100}} dB
  = -0.4575 dB
## P3-16. The attenuation of a signal is -10 dB. What is the final signal power if it was originally 5 W?
Attenuation = 10 {log} rsub {10} {{p} over {5}} = -10
or, p = 0.5 W
## P3-17. A signal has passed through three cascaded amplifiers, each with a 4 dB gain. What is the total gain? How much is the signal amplified?
Here the Number of Amplifier= 4
Total Gain = 4x3 = 12dB
If we consider the first signal and second signal to be P1 and P2, then,
12 = 10 log ( P_2 over P_1 )
or, P_2 over P_1 = 15.85
So the signal will be 15.85 times stronger than before.
## P3-18. If the bandwidth of the channel is 5 Kbps, how long does it take to send a frame of 100,000 bits out of this device?
Transmission time = 100,000 div 5000 = 20 seconds
## P3-19. The light of the sun takes approximately eight minutes to reach the earth. What is the distance between the sun and the earth?
Distance = 8 times 60 times 3 times 10 ^ 8 = 1.44 times 10^11 m .
## P3-20. A signal has a wavelength of 1 μm in air. How far can the front of the wave travel during 1000 periods?
Distance = N x λ = 1 μm x 1000 = 1000 μm = 1 mm
## P3-21. A line has a signal-to-noise ratio of 1000 and a bandwidth of 4000 KHz. What is the maximum data rate supported by this line?
Capacity = B times log_2( 1 + SNR )
= 4000 times log_2( 1+1000 )
= 39868.905035343974 kbps or, approximately 40 Mbps.
## P3-22. We measure the performance of a telephone line (4 KHz of bandwidth). When the signal is 10 V, the noise is 5 mV. What is the maximum data rate supported by this telephone line?
Capacity = B times log_2( 1 + SNR )
= 4000 times log_2( 1+ 10 over { 5 times 10^-3 } )
= 43866.021807622965 kbps
## P3-23. A file contains 2 million bytes. How long does it take to download this file using a 56-Kbps channel? 1-Mbps channel?
File size=2 million bytes=2000000 x 8 bits=16,000,000 bits
If the channel speed is= 56,000 bps
Required time is = 16,000,000 over 56,000 = 285.714 s
If the channel speed is= 1,000,000 bps
Required time is = 16,000,000 over 1,000,000 = 16 s
## P3-24. A computer monitor has a resolution of 1200 by 1000 pixels. If each pixel uses 1024 colors, how many bits are needed to send the complete contents of a screen?
Here, each pixel uses 1024 colors. So if we assume we need n bits,
so we can write, 2 ^ n = 1024
or, n = 10 bits.
Needed bits are = 1200x1000x10 = 12,000,000bits or, 12 Mb.
## P3-25. A signal with 200 milliwatts power passes through 10 devices, each with an average noise of 2 microwatts. What is the SNR? What is the SNRdB?
Here, as signal pass through 10 devices,
Signal for per device= 200 div 10 = 20 mW.
SNR = 20 times 10 ^ -3 over { 2 times 10 ^ -6 } = 10,000
SNR_dB = 10 log_10 10,000 = 40
## P3-26. If the peak voltage value of a signal is 20 times the peak voltage value of the noise, what is the SNR? What is the SNRdB?
SNR = { Signal power } over { Noise power } = { Signal voltage }^2 over { Noise voltage }^2 = 20^2 over 1^2 = 400
SNR_dB = 10 times log_10 SNR = 10 log_10 400 = 26.02 dB
## P3-27. What is the theoretical capacity of a channel in each of the following cases?
a. Bandwidth: 20 KHz SNRdB = 40
b. Bandwidth: 200 KHz SNRdB = 4
c. Bandwidth: 1 MHz SNRdB = 20
We know that,
SNR_dB = 10 times log_10 ( SNR )
or, SNR = 10^ {SNR_dB over 10}
So, Capacity, C = B log_2 ( 1 + 10^ {SNR_dB over 10} )

For bandwidth 20 kHz and SNRdB = 40
Capacity, C = 20,000 log_2 ( 1 + 10^ {40 over 10} ) = 265757.13 bps
For bandwidth 200 kHz and SNRdB = 4
Capacity, C = 200,000 log_2 ( 1 + 10^ {4 over 10} ) = 362449.24 bps
For bandwidth 1 MHz and SNRdB = 20
Capacity, C = 1000,000 log_2 ( 1 + 10^ {20 over 10} ) = 6658211.48 bps
## P3-28. We need to upgrade a channel to a higher bandwidth. Answer the following questions:
a. How is the rate improved if we double the bandwidth?
→ As the relationship is Capacity, C = B log_2 ( 1 + SNR ) , if we double the bandwidth then we will also improve the rate if SNR is constant.
b. How is the rate improved if we double the SNR?
→ As the relationship is Capacity, C = B log_2 ( 1 + SNR ) , here is a logarithmic relationship between C and SNR. So doubling the SNR will also increase the capacity.
## P3-29. We have a channel with 4 KHz bandwidth. If we want to send data at 100 Kbps, what is the minimum SNRdB? What is the SNR?
We know Capacity, C = B log_2 ( 1 + SNR )
or, 100,000 = 4000 times log_2 ( 1 + SNR )
or, SNR = 2 ^ ( 100,000 over 4000 ) - 1
or, SNR = 33554431
And, SNR_dB = 10 times log_10 ( SNR ) = 10 times log_10 ( 33554431 ) = 75.26
## P3-30. What is the transmission time of a packet sent by a station if the length of the packet is 1 million bytes and the bandwidth of the channel is 200 Kbps?
Packet size = 1,000,000 times 8 = 8,000,000 bits
Bandwidth = 200 Kbps = 200 times 10^3 bps
Required time = { Total data } over { Bandwidth } = 8 times 10^6 over { 200 times 10^3 } = 40 seconds.
## P3-31. What is the length of a bit in a channel with a propagation speed of 2 × 108 m/s if the channel bandwidth is
a.1Mbps
b.10Mbps
c.100Mbps

We know,
bit length = propagation speed x bit duration,
So, for 1 Mbps, bit length = 2 times 10^8 times { 1 over 1,000,000 } = 200 m.
For 10 Mbps, bit length = 2 times 10^8 times { 1 over 10,000,000 } = 20 m.
For 10 Mbps, bit length = 2 times 10^8 times { 1 over 100,000,000 } = 2 m.
## P3-32. How many bits can fit on a link with a 2 ms delay if the bandwidth of the link is
1. 1 Mbps
2. 10 Mbps
3. 100 Mbps
  Number of bits = bandwidth x delay
a. For 1 Mbps = 1x {10} ^ {6} x2x {10} ^ {-3} =2000 bits
b. For 10 Mbps = 10x {10} ^ {6} x2x {10} ^ {-3} =20,000 bits
c. For 100 Mbps = 100x {10} ^ {6} x2x {10} ^ {-3} =200,000 bits
## P3-33. What is the total delay (latency) for a frame of size 5 million bits that is being sent on a link with 10 routers each having a queuing time of 2 μs and a processing time of 1 μs. The length of the link is 2000 Km. The speed of light inside the link is 2 × 108 m/s. The link has a bandwidth of 5 Mbps. Which component of the total delay is dominant? Which one is negligible?
Processing time = 10 times 1 times 10 ^ -6 = 0.00001 s
Queuing time = 10 times 2 times 10 ^ -6 = 0.00002 s
Transmission time = {5times10^6 bits} over { 5 times 10^6 bps } = 1 s
Propagation time = { 2000 km } over { 2 times 10^8 m s^-1 } = 0.01s
Hence, total time = 0.00001 + 0.00002 + 1 + 0.01 = 1.01003 s

Here the transmission time is dominant because the packet size is huge. And the processing or queuing time is negligible.

--
SOMETIMES ignorance is a bliss ✨