## Slide 1: Introduction to Data Communications and Computer Networks
CCE 211 Data Communications and Engineering
Revised 2018-08-10
Arpita Howlader
Prof. Dr. Md. Samsuzzaman

## Slide 2: Reference Book
Data Communication and Networking - Behrouz A. Forouzan Latest Edition
Data and Computer Communication - William Stallings Latest Edition

## Slide 3: Outline
Communications Model
Basic Data Communication Terminology
Networking
Standards Organizations

## Slide 4: Telecom vs. Datacom
Communications
  Transfer of data from one entity to another via some form of transmission medium
Telecommunications
  Communication over a distance by definition
  All type of communications using signaling such as voice (telephone), images (television), data (computers)
Data communications
  Subset of telecommunications that involves the transmission and reception of data to and from computers and components of computer systems

## Slide 5: Data Communication: Definition
Data Communication:
Transfer of data from one device to another via
some form of transmission medium.
The term telecommunication means communication at a distance.
The word data refers to information presented in whatever form is agreed upon by the parties creating and using the data.

## Slide 6: Fundamental characteristics Data Communication

## Slide 7: Data Communication
Hi, how are you?
01010001
Hi, how are you?
Computer
you?
how
are
Hi,
you?
how
are
Hi,
01010001

## Slide 8: Communication Model
input message
Communications
system
Source system
Destination system
Source
Device
Transmitter
Transmission
medium
Receiver
Destination
device
input data
transmitted
signal
received
signal
output data
output message
Notes: The fundamental purpose of data communications is to exchange information between two parties. The source device generate the data to be transmitted. The transmitter transform and encodes the input data into the appropriate form of signals that can be transmitted across the transmission medium. The receiver accepts the signal and converts it into a from that can be handled by the destination device.

## Slide 9: Example of Communication System
Telephone Networks
Source system
Destination system
A
110011
110011
A
computer
modem
modem
computer
Notes: The fundamental purpose of data communications is to exchange information between two parties. The source device generate the data to be transmitted. The transmitter transform and encodes the input data into the appropriate form of signals that can be transmitted across the transmission medium. The receiver accepts the signal and converts it into a from that can be handled by the destination device.

## Slide 10: Components in Communication
Hi, how are you?
5
Protocol
4
Medium
3
Receiver
2
Sender
1
Message

## Slide 11: Components of Data Communications
message
Communications
system
Source system
Destination system
Source
Device
Transmitter
Transmission
medium
Receiver
Destination
device
input data
transmitted
signal
received
signal
output data
message
1
2
3
4
5
Protocol

## Slide 12: 1.1.2 Message -Data Representation
Numbers
  8/16/32 bit integers, signed/unsigned
  floating-point
Text
  ASCII, Unicode
Images
  Bit patterns, Graphics formats JPG, PNG, etc.
Audio  Samples of continuous signal
Video  Sequence of bitmap images
150
2
255

## Slide 13: Protocols and Standards
Protocol
  A set of rules governing data communications
    Syntax: format of data block
    Semantics: meaning of each section
    Timing: speed and sequencing
Standard
  De facto (in practice) standards
     not approved but widely adopted
  De jure (in law) standards
     approved by an organization

## Slide 14: Examples of Standards Organizations
List of some major standard bodies

## Slide 15: ITU-T
International standard organization that develops standard for telecommunications
Some well known standards
  V series
  X series
  H series
  G Series
International Telecommunications Union – Telecommunication Standard Sector

## Slide 16: ISO
An International standard organization that develops standard for variety of fields
International Standards Organization

## Slide 17: IETF
A large open international community of network designers, operators, vendors, and researchers concerned with the evolution of the Internet architecture
Internet Engineering Task Force

## Slide 18: IEEE
The largest professional group involved in standards for computing, communications, electrical and electronics
Institute of Electrical and Electronics Engineers

## Slide 19: Direction of Data Transmission
Simplex
Half-duplex
Type of Direction
Full-duplex
1.1.3 Data Flow
Notes: The signal is received will differ from the signal that is transmitted due to various transmission impairments. For analog signal, these impairments cause various modifications that degrade the signal quality. For digital signal, A binary 1 may be changed into a binary 0 and vice versa due to bit error.

## Slide 20: Simplex
Unidirectional
Computer
Display
Hi….
pager
Transmitter
Data are only transmitted in one direction
One device can only transmit; the other can only receive

## Slide 21: Half-duplex
Both stations may transmit; but only one at a time (alternate in transmitting)
Example: Walkie-Talkies
Transmit from S1 to S2 at time T1
Transmitter/Receiver
Transmitter/Receiver
Transmit from S2 to S1 at time T2
S2
S1

## Slide 22: Full-duplex
Full-Duplex operation can occur in two ways:
  two separate transmission path
  channel is divided between signals traveling in opposite directions
Example: telephones
Simulteneous send and receive
data from each other
Transmitter/Receiver
Transmitter/Receiver
S2
S1

## Slide 23: Networks
A network is a set of two or more devices connected through a communication system
Communication System
Cliparts are taken from http://openclipart.org

## Slide 24: Network Criteria
A network must be able to meet a certain number of criteria. The most important of these are
performance,
reliability, and
security.

## Slide 25: Line Configurations
Point-to-Point
Multipoint
Line configurations
Physical Structures
Type of Connection
A network is two or more devices connected through links. A link is a communications pathway that transfers data from one device to another. For communication to occur, two devices must be connected in some way to the same link at the same time.

## Slide 26: Point-to-Point
Only two devices share the medium
The entire capacity of the link is reserved for the transmission between those two devices
Station
Station
A direct link
between two devices
A direct link
between two devices

## Slide 27: Multipoint (or Multidrop)
More than two devices share the same medium
The capacity of the link is shared
Station
Station
A link is shared
between several devices
Station
Station
Station

## Slide 28: Data Transmission
Parallel
Serial
Asynchronous
Data Transmission
Synchronous

## Slide 29: Parallel Transmission
Simultaneous transmission results in high speed
Required more data lines, hence higher cost
Usually limited to short distances because its costs and crosstalk
Need eight data lines
for sending each byte
0
1
0
1
1
0
1
1
Picture from Wikipedia

## Slide 30: Serial Transmission
One bit follows another, only one data line for each direction
The sender needs a parallel-to-serial converter and the receiver needs a serial-to-parallel converter.
Need only one data line
0101101110
0100101110
0000101110
0110101110
A group of bits are sent one after another

## Slide 31: Network Topologies
Common topologies are bus, ring, star, and mesh
Network Topologies
Bus
Star
Mesh
Ring

## Slide 32: Topology
Topology: physical or logical arrangement of devices
  Point-to-point
  Mesh
  Star
  Bus
  Ring
  Hybrid

## Slide 33: Point-to-Point Connection

## Slide 34: Fully Connected Mesh Topology
A
C
B
D
E

## Slide 35: Fully Connected Mesh Topology

## Slide 36: Fully Connected Mesh Topology
Pros:
  Dedicated links
  Robustness
  Privacy
  Easy to identify fault
Cons:
  A lot of cabling
  I/O ports
  Difficult to move

## Slide 37: Star Topology
Hub
A
D
B
C
Drop
Drop

## Slide 38: Star Topology
Switch
A
D
B
C

## Slide 39: Star Topology
Hub
A
D
B
C

## Slide 40: Star Topology
Pros:
  One I/O port per device
  Little cabling
  Easy to install
  Robustness
  Easy to identify fault
Cons:
  Single point of failure
  More cabling still required
Hub

## Slide 41: Bus Topology
Drop line
Tap
Terminator

## Slide 42: Bus Topology
A
B
C
D

## Slide 43: Bus Topology

## Slide 44: Bus Topology
Pros:
  Little cabling
  Easy to install
Cons:
  Difficult to modify
  Difficult to isolate fault
  Break in the bus cable stops all transmission

## Slide 45: Ring Topology
A
B
C
D

## Slide 46: Ring Topology

## Slide 47: Ring Topology
Pros:
  Easy to install
  Easy to identify fault
Cons:
  Delay in large ring
  Break in the ring stops all transmission

## Slide 48: Hybrid Topologies

## Slide 49: Switching Networks
Communication Network
Communications is achieved by transmitting
data from source to destination through a
network of switching nodes
Communication Network Node
Network Station
end node (source &destination)
provide switching facility (routing)

## Slide 50: Switching Technologies
Circuit switching
  A circuit is established for the two parties
Packet switching
  Data are put into packets, each stamped with source and destination addresses
  Routers know where to forward packets
telephone switch
Router
Packet

## Slide 51: Key Differences
Aspect | Circuit Switching | Packet Switching
Data path | Dedicated single route | Different shared routes
Message | Bypass | Temporarily stored at each node
End point's status | Both must be ready | Only sender is ready
Utilization | Poor | Good
Data rate | Fixed | Varied
Prioritization | Not support | Support

## Slide 52: Network Categories by Distance
Network categories (by distance)
Local Area Network (LAN)
Wide Area Network (WAN)
Body/Personal Area Network (BAN/PAN)
Metropolitan Area Network (MAN)
Notes: The signal is received will differ from the signal that is transmitted due to various transmission impairments. For analog signal, these impairments cause various modifications that degrade the signal quality. For digital signal, A binary 1 may be changed into a binary 0 and vice versa due to bit error.

## Slide 53: LAN
hub/switch
hub/switch
hub/switch
hub/switch
router
General Characteristics :
Confined geographical area
Under single management
High data rate
servers
stations
stations
stations
Notes: Communications network that serves users within a confined area is known as a Local Area Network (LAN). Computers (server and workstations) are normally distributed around a single office or building, including network device like hub, bridge or router.

## Slide 54: MAN
A network which cover an entire city
A single network or a number of connected LANs
Public city
network
LAN
LAN
LAN
LAN
Notes: Data communication takes place between two devices that are connected. It is impractical for any two devices to be directly, point-to-point connected because of :
- The devices are very far apart.
- Some device may require a link to many of the others.
The solution is to attach each device to a network. The devices are known as stations or network stations. The stations may be computer or other communicating devices. Each station attaches to a network node, which performs communication tasks.
เครือข่ายโทรศัพท์สาธารณะ (Public Switched Telephone Network : PSTN)
แลน (Local Area Network : LAN)
สายเช่า (Leased lines)
เครือข่ายข้อมูลสาธารณะ (Public Switched Data Network : PSDN)
เครือข่ายบริการร่วมดิจิตัล (Integrated Services Digital Network : ISDN)

## Slide 55: WAN
A network that covers a relatively broad geographic area
It often uses long-distance transmission facilities provided by public carriers

## Slide 56: BAN/PAN
http://developer.sonymobile.com
Nike.com
https://www.bhphotovideo.com/images/images1000x1000/Adesso_IMOUSE_S100_Bluetooth_Mini_Optical_Scroll_696816.jpg

## Slide 57: Network of Networks
Company A
Company D
Network Interface Card (NIC)
Company B
Company C

## Slide 58: Internetworking
How to allow devices of different standards to communicate?
Gateways/routers – devices capable of communicating in several standards
These become "network of networks", i.e., internetwork

## Slide 59: Internetworks
Collection of networks interconnected by routers and other devices
LAN
LAN
LAN
LAN
MAN
WAN
LAN

## Slide 60: The Internet
The largest internetwork in the world
Devices communicating with TCP/IP protocol suite
UCLA
Stanford
UC Santa Barbara
U. of Utah

## Slide 61: Internet Growth
https://devcentral.f5.com/articles/security-sidebar-defending-the-internet-of-things

## Slide 62: Technologies Around Us
New generation of switching technologies provide improved services to home and workplace
Frame Relay
Network
ATM
Network
ISDN
Network
Internet
E/T-carrier
Cable Modem
ADSL
CATV
PSTN
Network
Modem
Cellular 3G/4G/5G
Notes: Public carrier circuit have been normally used for connected computers in different sites,. The resulting network is known as a Wide Area Network (WAN). One approach is to lease transmission lines from the public carriers and install a private switching system at each site to create an Enterprise Wide Private Network. Such networks normally incorporate both voice and data communications.
The benefits are such as communication channel is private and online, several data transmission rate is provided from low speed to high speed.

## Slide 63: Summary
Data communications
  Protocols and standards
  Data flows
  Connectivity
Computer networks
  Topologies
  LAN/MAN/WAN/BAN/PAN
Internetworks (networks of networks)
The Internet