# EEE | Practice problems (3-phase)
## 12.1 Given that V _ bn = 110 ∠ 30 , find Van and Vcn, assuming a positive (abc) sequence.
Van’s angle – 120 = Vbn’s angle

## 12.2 A Y-connected balanced three-phase generator with an impedance of 0.4 + j0.3 ohm per phase is connected to a Y-connected balanced load with an impedance of 24 + j19 ohm per phase. The line joining the generator and the load has an impedance of 0.6 + j0.7 ohm per phase. Assuming a positive sequence for the source voltages and that Van = 120∠30 V, find: (a) the line voltages, (b) the line currents.
Line voltages = sqrt(3) x phase voltage + phase shift by ∠30
(a) for Vab (line vol) = sqrt(3) x 120 ∠(30+30) = 207.85∠60
অনুরূপভাবে, Vbc = 207.85∠(60-120)
Vca = 207.85∠(60-(2x120)) অথবা, 207.85∠(60+120)
^ (বই এ এভাবে করা আছে যদিও)
Line current = Phase current = I_ab = V_ab over { 0.4 + j0.3 + 24 + j19 + 0.6 + j0.7 } = { 120 ∠ 30 } over { 0.4 + j0.3 + 24 + j19 + 0.6 + j0.7 } = 3.7∠-8.66 A
Likewise, { { I _ { bc ~ } = 3.7 } ~ ∠ { ~ - 128.66 } } , { { I _ { ca ~ } = 3.7 } ~ ∠ { ~ 111.34 } }
# 12.3 One line voltage of a balanced Y-connected source is VAB = 240l∠20 V. If the source is connected to a dell-connected load of 20∠40 ohm, find the phase and line currents. Assume the abc sequence.
Phase current,
Iab = {240∠-20} over {20∠40} = 12∠-60
{ I _ BC { ~ = ~ } } 12∠( -60 - 120 ) = 12∠-180
{ I _ CA { ~ = ~ } } 12∠( -60 + 120 ) = 12∠60
Line currents,
Ia = sqrt(3) x Iab x ∠(-30) = sqrt(3) x 12 ∠(-60-30) = 20.78 ∠ -90 A
Ib = 20.78 ∠-210
Ic = 20.78 ∠ 30

# 12.4 A positive-sequence, balanced delta-connected source supplies a balanced delta-connected load. If the impedance per phase of the load is 18+ j12 ohm and Ia = 19.202∠35 A, find IAB and VAB.
IAB = 19.202 over sqrt( 3 ) ∠ 35+30 = 11.086∠65 A (Line → Phase)
VAB = I _ AB times Z_%DELTA = (11.086∠65) times (18+j12)=239.827∠98.69

# 12.5 In a balanced Dell-Y circuit, Vab = 240∠15 and ZY = (12 + j15) ohm. Calculate the line currents.
Van = V _ { ab ~ } over sqrt 3 ∠-30 = 240 over sqrt 3 ∠(15-30) = 138.56∠-15
Ia = V_an over Z_Y = { 138.56 ∠ -15 } over { 12 + j15 } = 7.21 ∠ -66.34
Ib = 7.21 ∠ (-66.34-120)
Ic = 7.21 ∠ (-66.34+120)

# 12.6 For the Y-Y circuit in Practice Prob. 12.2, calculate the complex power at the source and at the load.
At the source,
Ss = -3 VpIp* = -3 x 120∠30 x 3.75∠8.66 = -1054.17007-843.34j VA
Sl = 3 x |Ip|2 x Vl = 3 x 3.752 x (24+j19) = 1012.5 + j801.56

# 12.7 Calculate the line current required for a 30-kW three-phase motor having a power factor of 0.85 lagging if it is connected to a balanced source with a line voltage of 440 V.
P = S cosθ
or, S = 30k / 0.85 = 35294.12 W
And, S = sqrt(3) x VL x IL
or, IL = { S over {sqrt 3 V_L} } = 35294.12 over { sqrt 3 times 440 } = 46.31 A
# 12.8 Skipped
# 12.9 The unbalanced ¢-load of Fig. 12.24 is supplied by balanced line-to-line voltages of 240 V in the positive sequence. Find the line currents. Take Vab as reference.

Phase current,
{ { { { I _ AB = { V _ AB over { { 10 - 5 } j } } } = { { 240 ∠ 0 } over { { 10 - 5 } j } } } = 21.46 } ∠ 26.56 } newline { { { I _ BC = { { 240 ∠ -120 } over { { 16 } j } } } = 15 } ∠ -120 } newline { { { I _ CA = { { 240 ∠ 120 } over { { 8+6 } j } } } = 24 } ∠ 83.13 }
Line current,
I_a = I_AB - I_CA = 21.46∠26.56-24∠83.13 newline = 21.66∠-41.08 A
I_b = I_BC - I_AB = 15∠-120-21.46∠26.56 ~ =~ 34.88∠-140.36 A
I_c = I_CA - I_BC = 24∠83.13-15∠-120 ~ =~ 38.25∠74.27 A