## Slide 1: Network Models and Protocol Suites
Based on lecture materials from Data Communications and Networking, 5th ed., Behrouz A. Forouzan, McGraw Hill, 2012.
Revised 2019-07-28
CCE 211 Data Communications and Engineering
Prof. Dr. Md. Samsuzzaman

## Slide 2: Outline
Communication abstraction
Layered tasks
Internet protocol suites
ISO's OSI model

## Slide 3: Layered Tasks
Computer networks are complex systems
  Tasks involve varieties of hardware and software components, and protocols
Networking task is divided into several subtasks, or layers

## Slide 4
Figure 2.1: A single-layer protocol

## Slide 5
Figure 2.2: A three-layer protocol

## Slide 6
2.1.2 Principles of Protocol Layering
Let us discuss two principles of protocol layering.
The first principle dictates that if we want bidirectional communication, we need to make each layer so that it is able to perform two opposite tasks, one in each direction.
The second principle that we need to follow in protocol layering is that the two objects under each layer at both sites should be identical.

## Slide 7
2.1.3 Logical Connections
After following the above two principles, we can think about logical connection between each layer as shown in Figure 2.3. This means that we have layer-to-layer communication. Maria and Ann can think that there is a logical (imaginary) connection at each layer through which they can send the object created from that layer. We will see that the concept of logical connection will help us better understand the task of layering we encounter in data communication and networking.

## Slide 8
Figure 2.3: Logical connection between peer layers

## Slide 9: Real-Life Example
Communication takes place thru many entities
Logical communication
Secretary: types a letter
Delivery boy: drops the letter
Secretary: reads and reports the message
Delivery boy: takes the letter
Post office:
Processes and routes the letter
Postal truck

## Slide 10: Layer Model
Layer N uses services provided by Layer N-1
Layer N
Layer N
Using services
Providing services
Logical communication path
HOST A
HOST B
Layer N-2
Layer N-2
Layer N-1
Layer N-1
Virtual Communication System
Layer N protocol

## Slide 11: Why Layers?
Guidelines for protocol developments
  Reference model
Modularity
  Eases maintenance and updating of systems
  A change in one layer is transparent to the rest
Is layering always the best thing to do?
  Maybe not  cross-layer optimization

## Slide 12
Figure 2.5: Communication through an internet

## Slide 13: Communication Abstraction
A
B
Application-to-application communication
application process
application process

## Slide 14: Communication Abstraction
A
B
Internet
End-to-end data transport over the Internet
Transport service

## Slide 15: Communication Abstraction
Internet
Data routing service over the Internet
router

## Slide 16: Communication Abstraction
Node-to-node delivery
link
link
link

## Slide 17: Communication Abstraction
Image by OpenClipArt-Vectors from Pixabay
Wireless
Multipoint
Point-to-point link (optical fiber, copper, etc)
NIC (Network Interface Card)
Signal transmitted over physical media

## Slide 18: Internet Layer Model/TCP IP layer
The Internet Protocol Stack
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
User
Transmission Medium
Hardware
Software

## Slide 19: Application Layer
The only layer to interact with users
Responsible for providing services to the user application
SMTP
HTTP
FTP
SMTP
HTTP
FTP
Data
Data
H5
Application Layer
Data
H5
Data
Logical communication
Transport Layer
(source)
(destination)

## Slide 20: Transport Layer
Duties/services
  Port addressing
  Segmentation and reassembly
  Connection control
  Flow control (end-to-end)
  Error control (end-to-end)
Responsible for delivery of a message from one process to another

## Slide 21: Transport Layer
Transport Layer
Data
Data1
Data2
Data3
H4
H4
H4
Data
Data1
Data2
Data3
H4
H4
H4
(segments)
Process
Process
…
Process
Process
…
PORT #
PORT #
Network Layer
(source)
(destination)

## Slide 22: Network Layer
Duties/services
  Logical addressing
  Routing
Responsible for the delivery of packets from the original source to the destination

## Slide 23: Network Layer
router
router
Segment
from Transport
Segment
to Transport
Segment
H3
Segment
H3
(packet)
Data Link Layer
decide which outgoing interface to use
Segment
H3
Segment
H3
Data Link Layer
Data Link Layer
(source)
(destination)

## Slide 24: Network Layer Operation
Network A
Network B
Network C
A.1
A.2
B.6
B.1
B.3
C.7
C.2
Network D
D.8
D.3
Router
Segment
A1
C7
A.1, A.2, B.1, B.3, ... are logical addresses
R1
R3
R2
A.5
B.7
B.2
D.1
B.9
C.3
Segment
A1
C7
Segment
A1
C7
Segment
A1
C7
To transport layer
From transport layer

## Slide 25: Data Link Layer
Duties/services
  Framing
  Physical addressing
  Flow control (hop-to-hop)
  Error control (hop-to-hop)
  Access control
Responsible for transmitting frames from one node to the next

## Slide 26: Data Link Layer
Data Link Layer
Packet
from Network
Packet
to Network
Packet
H2
Packet
H2
(frame)
T2
T2
Physical Layer

## Slide 27: Data Link Layer
3B
9F, 3B, 82, 6D, ... are physical addresses
9F
82
6D
Packet
9F
T2
6D
Packet
H2

## Slide 28: Data Link Layer Operation
Network A
Network B
Network C
A.1
A.2
B.6
B.1
B.3
C.7
C.2
Network D
D.8
D.3
Sgmt
A.1
C.7
97
32
25
79
62
54
74
12
88
Sgmt
A.1
C.7
25
97
Sgmt
A.1
C.7
62
79
Sgmt
A.1
C.7
74
54
R1
R3
R2
Sgmt
A.1
C.7
74
54
To network layer
A.5
B.7
B.2
D.1
B.9
C.3

## Slide 29: Physical Layer
Duties/services
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate (transmission rate)
  Synchronization of bits
Responsible for transmitting individual bits from one node to the next

## Slide 30: Physical Layer
Frame
from Data Link
to Data Link
Frame
01001011
01001011
Transmission medium
(bits)

## Slide 31: The Big Picture
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111011010101001010101001
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111010101010010101010101
5
4
3
2
1
5
4
3
2
1
Transmission medium

## Slide 32: Layers and Addresses

## Slide 33: Layers and Types of Data Delivery

## Slide 34: Internet Model
Application
Transport
Network
Data Link
Physical
Network
D.L.
P.L.
D.L.
P.L.
Network
D.L.
P.L.
D.L.
P.L.
Application
Transport
Network
Data Link
Physical
Transmission medium
source
router
router
destination

## Slide 35: Protocol Suites
A set of protocols must be constructed
  to ensure that the resulting communication system is complete and efficient
Each protocol should handle a part of communication not handled by other protocols
How can we guarantee that protocols work well together?
  Instead of creating each protocol in isolation, protocols are designed in complete, cooperative sets called suites or families
Notes: 35

## Slide 36: Internet Protocol Suite
Layer | Protocols
Application | HTTP, FTP, Telnet, SMTP, ...
Transport | TCP, UDP, SCTP, ...
Network | IP (IPv4), IPv6, ICMP, IGMP, ...
Data Link | Ethernet, Wi-Fi, PPP, ...
Physical | RS-232, DSL, 10Base-T, ...

## Slide 37: OSI Model
OSI – Open Systems Interconnection
Developed by the International Standards Organizations (ISO)
Two additional layers
  Presentation layer
  Session layer
7.Application Layer
6.Presentation Layer
5.Session Layer
4.Transport Layer
3.Network Layer
2.Data Link Layer
1.Physical Layer
User
Transmission Medium

## Slide 38: OSI Layers in Real World
transmission medium
Reads the message
Summarizes or translates letter
Opens letter
Withdraws letter from mailbox
Checks address and sorts letter
Unpacks packages
Unloads from truck
Handwrites a message
7.Manager
Prepares final version
6.Assistant
Provides address and packs letter
5.Secretary
Delivers letter to post office
4.Driver
Checks address and sorts letter
3.Postal staff
Packs letters for certain directions
2.Postal staff
Loads on truck
1.Postal staff
Pictures from Wikipedia

## Slide 39: Session Layer
Duties/services
  Interaction management
     Simplex, half-duplex, full-duplex
  Session recovery
Responsible for establishing, managing and terminating connections between applications

## Slide 40: Presentation Layer
Duties/services
  Data translation
  Encryption
  Decryption
  Compression
Responsible for handling differences in data representation to applications

## Slide 41: Summary
Layered tasks are used for abstracting complex communication details
Layer models were created for reference
  Internet model (5 layers)
  ISO's OSI model (7 layers)
Protocol suite is a collection of protocols operating at various layers