## Slide 1
ITS323/CSS331
Transmission
Media
Media and
Spectrum
Transmission Media
Guided Media
Wireless
Transmission
Antennas
Propagation
Wireless Examples

## Slide 2
ITS323/CSS331
Contents
Transmission
Media
Transmission Media and Spectrum
Media and
Spectrum
Guided Media
Wireless
Transmission
Guided Media
Antennas
Propagation
Wireless Transmission
Wireless Examples
Antennas and Antenna Gain
Propagation and Path Loss
Wireless Examples

## Slide 3
Transmission Media
All computer communication involves encoding data in a form of energy, and sending the energy across a transmission medium (i.e., the network links).
Guided and Unguided Media
Links can be categorized by the type of path used:
  Guided Media: communication follows an exact path (such as a wire)
  Unguided Media: communication follows no specific path (such as a radio transmission)
Forms of Energy
Links can be categorized by the type of energy used for transmission:
  Electrical Energy is used on wires
  Radio Frequency Transmission is used for wireless
  Light is used for optical fibers and lazers

## Slide 4
Taxonomy by Forms of Energy

## Slide 5
ITS323/CSS331
Transmission Media
“the thing between the transmitter and receiver”
Transmission
Media
Media and
Spectrum
Signal propagates from transmitter to receiver via some
medium
Which medium should be used?
I
Guided Media
I
Wireless
Transmission
Maximise data rate
Maximise distance
Minimise bandwidth
Minimise transmission impairments
Minimize cost
�
�
�
�
�
Antennas
Propagation
Wireless Examples
Guided (wired) vs unguided (wireless)
I

## Slide 6: Physical Layer

## Slide 7
ITS323/CSS331
Signals and Spectrum
Transmission
Media
Communication signals contain components with
different frequencies, spectrum of signal
Often refer to center frequency and bandwidth of signal
I
Media and
Spectrum
I
Guided Media
Wireless
Transmission
S(f)
Antennas
70%
Propagation
Wireless Examples
andwidth
f
low centre cutoff
high cutoff
Electromagnetic spectrum is used by many applications
International and national authorities regulate usage of spectrum
Aim: minimize interference between applications/users, while allowing many applications/users
I
I
I
b

## Slide 8
ITS323/CSS331
Electromagnetic Spectrum for Communications
Transmission
Media
Frequency [Hz]
100
Media and
Spectrum
103
106
109
1012 1015
1018 1021
Visible
Guided Media
Wireless
Transmission
Wavelength [m] 105
100
10−3 10−4
10−8
10−11
Antennas
Twisted Pair
Remote
WiFi
ADSL
Optical
Fibre
Propagation
FM
3G
AM
Satellite
TV
Coaxial Cable
Wireless Examples
ITU and IEEE bands:
VLF
LF
MF
HF
UHF
VHF
SHF
EHF
THF
3kHz 30kHz 300kHz 3MHz 30MHz 300MHz 3GHz 30GHz 300GHz 3THz
ITU
L S
C X K u
K
K a
1 2 4 8 12
18
27
40GHz
IEEE
Radio
Microwave
THz
Infrared
Ultraviolet
X−ray
Gamma
3kHz
300MHz 300GHz 3THz
30PHz
30EHz

## Slide 9
ITS323/CSS331
Contents
Transmission
Media
Transmission Media and Spectrum
Media and
Spectrum
Guided Media
Wireless
Transmission
Guided Media
Antennas
Propagation
Wireless Transmission
Wireless Examples
Antennas and Antenna Gain
Propagation and Path Loss
Wireless Examples

## Slide 10: Classes of Transmission Media

## Slide 11: Guided Media
Provide a conduit from one device to another
Include
  twisted-pair cables
  coaxial cables
  fiber-optic cables

## Slide 12
ITS323/CSS331
Electrical Cables
Transmission
Media
Transmit electrical signals on a conductor, e.g. copper
Cable carrying electrical current radiates energy, and can pick-up energy from other sources
I
I
Media and
Spectrum
Guided Media
Can cause interference on other cables
Other sources can cause interference on the cable
Interference results in poor quality signals being received
�
�
�
Wireless
Transmission
Antennas
Propagation
To minimise interference:
I
Wireless Examples
Keep the cable lengths short
Keep the cables away from other sources
Design the cables to minimise radiation and pick-up
�
�
�
Use materials to shield from interference
Organise multiple wires so they dont interfere with each other
�
�

## Slide 13
ITS323/CSS331
Twisted Pair
Transmission
Media
Two insulated copper wires arranged in spiral pattern
Most commonly used and least expensive medium
I
I
Media and
Spectrum
Used in telephone networks and in-building
communications
Telephone networks designed for analog signalling (but supporting digital data)
Also used for digital signalling
�
Guided Media
Wireless
Transmission
�
Antennas
Propagation
�
Wireless Examples
Two varieties of twisted pair: shielded (STP) and
unshielded (UTP); also multiple categories (CAT5)
I

## Slide 14: Twisted-Pair Cable

## Slide 15: UTP and STP Cables
UTP – Unshielded Twisted Pair
STP –Shielded Twisted Pair

## Slide 16: Categories of UTP/STP Cables

## Slide 17: Categories of UTP/STP Cables
Category | Bandwidth | Digital/Analog | Use
1 | very low | Analog | Telephone
2 | < 2 MHz | Analog/digital | 4Mbps token ring
3 | 16 MHz | Digital | 10-100 Mbps Ethernet
4 | 20 MHz | Digital | 16 Mbps token ring
5 | 100 MHz | Digital | 100 – 1000 Mbps Ethernet
5E | 100 MHz | Digital | 100 – 1000 Mbps Ethernet
6 | 250 MHz | Digital | 1 – 10 Gbps Ethernet
6A | 500 MHz | Digital | 1 – 10 Gbps Ethernet
7 | 600 MHz | Digital | 10 Gbps Ethernet
7A | 1000 MHz | Digital | 40-100 Gbps Ethernet

## Slide 18: UTP Connectors
RJ – Registered Jack

## Slide 19
ITS323/CSS331
Coaxial Cable
Transmission
Media
Two conductors, one inside the other
Provide much more shielding from interference than twisted pair: Higher data rates; More devices on a shared line; Longer distances
Widely used for cable TV, as well as other audio/video cabling
Used in long-distance telecommunications, although optical fibre is more relevant now
I
I
Media and
Spectrum
Guided Media
Wireless
Transmission
I
Antennas
Propagation
I
Wireless Examples

## Slide 20: Coaxial Cable

## Slide 21: Categories of Coaxial Cables
RG – Radio Government

## Slide 22: BNC Connectors
Bayonet Network Connector
  aka. Bayonet Neil-Concelman
Used with coaxial cables

## Slide 23: UTP and Coaxial Performance
www.ti.com/lit/an/sboa123/sboa123.pdf

## Slide 24
ITS323/CSS331
Optical Fibre
Transmission
Media
Light (optical rays) is guided within glass or plastic
fibres
Used in long-distance telecommunications, as well as telephone systems, LANs, and city-wide networks Advantages of optical fibre over electrical cables:
I
Media and
Spectrum
I
Guided Media
Wireless
Transmission
I
1.
2.
Lower loss: can transfer larger distances
Higher bandwidth: a single fibre is equivalent to 10’s or
100’s of electrical cables
Small size, light weight: lowers cost of installation
Electromagnetic isolation
Antennas
Propagation
Wireless Examples
3.
4.

## Slide 25: Optical Fiber
Based on physics of light

## Slide 26: Optical Fiber

## Slide 27: Propagation Modes
Multi-mode, step index
Multi-mode, graded index
Single-mode

## Slide 28: Fiber Types

## Slide 29: Fiber Construction

## Slide 30: Fiber-Optic Cable Connectors

## Slide 31: Optical Fiber Performance

## Slide 32
ITS323/CSS331
Comparison of Guided Media
Electrical Cables
Transmission
Media
Media and
Spectrum
Moderate data rates: lGb/s
Maximum distance: 2km (twisted pair); lOkm (coaxial)
Cheapest for low data rates
UTP: easy to install, susceptible to interference
STP, Coaxial Cable: rigid, protection against interference
I
Guided Media
I
Wireless
Transmission
I
Antennas
I
Propagation
Wireless Examples
I
Optical Cables
Very high data rates: lOOGb/s+
I
Maximum distance: 4Okm
Expensive equipment, but cost effective for high data rates
Difficult to install
I
I
I

## Slide 33
ITS323/CSS331
Contents
Transmission
Media
Transmission Media and Spectrum
Media and
Spectrum
Guided Media
Wireless
Transmission
Guided Media
Antennas
Propagation
Wireless Transmission
Wireless Examples
Antennas and Antenna Gain
Propagation and Path Loss
Wireless Examples

## Slide 34: Unguided Media: Wireless
Transport electromagnetic waves without using a physical conductor
  Radio Waves
  Microwaves
  Infrared
Often referred to as wireless communication

## Slide 35: Wireless Transmission Waves
used for multicast/broadcast communications, such as radio and television
used for unicast communication such as cellular telephones, satellite networks, and wireless LANs
used for short-range communication in a closed area using line-of-sight propagation

## Slide 36: Electromagnetic Spectrum

## Slide 37: Propagation Methods

## Slide 38: Bands

## Slide 39
ITS323/CSS331
Wireless Transmission Model
Common wireless systems for communications include:
Transmission
Media
Media and
Spectrum
Terrestrial microwave, e.g. television transmission
Satellite microwave, e.g. IPstar
Broadcast radio, e.g. IEEE 802.11 WiFi (wireless LAN) Infrared, e.g. in-home communications
I
Guided Media
I
Wireless
Transmission
I
Antennas
I
Propagation
Wireless Examples
Transmit
Antenna
Receive
Antenna
Signal
Transmitter
Receiver

## Slide 40
ITS323/CSS331
Wireless Transmission Model
Transmission
Media
G t
G r
Media and
Spectrum
P t
L
P r
Guided Media
Wireless
Transmission
Antennas
Propagation
Wireless Examples
Transmit electrical signal with power Pt
Tx antenna converts to electromagentic wave;
introduces a gain Gt
Signal loses strength as it propagates; loss L
Rx antenna converts back to electrical signal, gain Gr
I
I
I
I I
Receive signal with power Pr

## Slide 41
ITS323/CSS331
Contents
Transmission
Media
Transmission Media and Spectrum
Media and
Spectrum
Guided Media
Wireless
Transmission
Guided Media
Antennas
Propagation
Wireless Transmission
Wireless Examples
Antennas and Antenna Gain
Propagation and Path Loss
Wireless Examples

## Slide 42
ITS323/CSS331
Antennas
Transmission
Media
Antenna converts between electrical current and
electromagnetic waves
Waves are within the Radio and Microwave bands of 3 kHz to 300 GHz
Antenna characteristics are same for sending or receiving
Direction and propagation of a wave depends on antenna shape
Isotropic antenna: power propagates in all directions equally (spherical pattern, ideal)
Omni-directional antenna: power propagates in all directions on one plane (donut)
Directional antenna: power concentrated in particular direction
Power output in particular direction compared to power produced by isotropic antenna is antenna gain [dBi]
I
Media and
Spectrum
I
Guided Media
Wireless
Transmission
I
Antennas
I
Propagation
Wireless Examples
I
I
I
I

## Slide 43
ITS323/CSS331
Example:
Isotropic Antenna (2D)
Transmission
Media
Pr
Media and
Spectrum
Guided Media
Wireless
Transmission
1m
Antennas
Pt
Propagation
Wireless Examples
Transmit with power Pt
Measure received power lm away to be Pr
Received power is same at any point equidistant from transmitter (black circle)
I
I
I

## Slide 44
ITS323/CSS331
Example:
Directional Antenna (2D)
Transmission
Media
Pr
Media and
Spectrum
Guided Media
Pr
Wireless
Transmission
1m
Px
Antennas
Pt
Propagation
Wireless Examples
Gain = Px
Pr
Transmit with same power Pt
Blue shape: at each point, received power is Pr
Measure received power lm away to be Px
Gain of antenna (compared to isotropic) is Px /Pr
I
I
I
I

## Slide 45
ITS323/CSS331
Antenna Patterns
Transmission
Media
Media and
Spectrum
Guided Media
Wireless
Transmission
Antennas
Propagation
Wireless Examples
Isotropic
Dipole
Horn
Dipole
Sector

## Slide 46
ITS323/CSS331
Wireless Propagation
Transmission
Media
Frequency of signals affect how signal propagates
Different frequencies impacted by water, atmospheric noise, cosmic noise, temperature
I
I
Media and
Spectrum
Guided Media
Ground Wave
signal follows contour of Earth, e.g. AM radio
Wireless
Transmission
Antennas
Propagation
Wireless Examples
Sky Wave signal reflected between ionosphere and Earth,
e.g. amateur radio, international radio stations

## Slide 47
ITS323/CSS331
Contents
Transmission
Media
Transmission Media and Spectrum
Media and
Spectrum
Guided Media
Wireless
Transmission
Guided Media
Antennas
Propagation
Wireless Transmission
Wireless Examples
Antennas and Antenna Gain
Propagation and Path Loss
Wireless Examples

## Slide 48
ITS323/CSS331
Satellite Communications
Transmission
Media
Applications: TV broadcast, remote/marine
communications, positioning, private data networks, Internet
Configuration: point-to-multipoint; point-to-point
Orbits: geostationary (GEO, 36000km), low earth
(LEO, l00's km), . . .
Antennas: parabolic (dish), metre to l0's of metres
Frequency bands: C, Ka, Ku bands
See example of IPStar
I
Media and
Spectrum
Guided Media
I
Wireless
Transmission
I
Antennas
Propagation
I
Wireless Examples
I
I

## Slide 49
ITS323/CSS331
Terrestrial Wireless
Transmission
Media
Applications: long distance links, TV broadcast,
AM/FM, Internet
Configuration: point-to-point; point-to-multipoint
Example: IEEE 802.16 (WiMax)
I
Media and
Spectrum
I
I
Guided Media
Wireless
Transmission
11 GHz, 10-20 Mb/s, 10-20 km line of sight
�
Antennas
Propagation
Wireless Examples

## Slide 50
ITS323/CSS331
Mobile Phones
Transmission
Media
Applications: personal communications, Internet,
monitoring
Frequency bands: 2.1 GHz, 1.8/1.9 GHz, 85O/9OO MHz; licensed
Bandwidth: 5 MHz for 3G Distance: 1OO's of metres to kms Data Rates: 1OO's kb/s to 1O's Mb/s
I
Media and
Spectrum
I
Guided Media
Wireless
Transmission
I
Antennas
I
Propagation
Wireless Examples
I

## Slide 51
ITS323/CSS331
Local Networks
Transmission
Media
Applications: local area network, connect portable
devices
Standards: IEEE 8O2.ll (WiFi) a/b/g/n/ac/. . . ; Bluetooth
Frequency bands: 2.4 GHz and 5.2-5.7 GHz; unlicensed
Bandwidth: 2O MHz channels (increased for optional higher data rates)
Distance: metres to lO's of metres
Data Rates: lO's Mb/s to lOO's Mb/s
�
Media and
Spectrum
�
Guided Media
Wireless
Transmission
�
Antennas
�
Propagation
Wireless Examples
�
�